## Slide 1
DIGITAL DESIGN(DD)
INSTR F243/EEE F215 /ECE F215 /CS F215
16/09/2025- Tutorial # 6

## Slide 2
Q1. A PN flip-flop has four operations: set to 1, no change, complement, and clear to 0, when inputs P and N are 00, 01, 10, and 11, respectively.
Tabulate the characteristic table.
Derive the characteristic equation.
Tabulate the excitation table.
The truth table for PN flip-flop is
P | N | Qn+1
0 | 0 | 1
0 | 1 | Qn
1 | 0 | Qn’
1 | 1 | 0

## Slide 3
 | P | N | Qn | Qn+1
0 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 
2 | 0 | 1 | 0 | 
3 | 0 | 1 | 1 | 
4 | 1 | 0 | 0 | 
5 | 1 | 0 | 1 | 
6 | 1 | 1 | 0 | 
7 | 1 | 1 | 1 | 
1
1
0
1
1
0
0
0
 | 00 | 01 | 11 | 10
0 | 0 | 1 | 3 | 2
1 | 4 | 5 | 7 | 6
P
NQn
Qn+1
1
1
1
1
characteristic table
Qn+1=N’Qn’ + P’Qn
characteristic equation

## Slide 4
Excitation table
Qn | Qn+1 | P | N
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0
1
1
0

## Slide 5
Q2. For the following sequential circuit, construct the state table and state diagram. Also, state whether it is a Mealy or Moore machine?

## Slide 9
(a)
(i) Find the Boolean expressions for the JK flip-flop inputs

## Slide 10
Q1 | Q2 | X | J1 | K1 | J2 | K2 | Q1+ | Q2+ | Z
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
0
1
0
0
0
1
0
0
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
0
0
1
0
1
0
0
0
0
1
1
1
1
0
1
0
0
1
0
1
0
0
0
1
0
0
1
1
0
(ii) Use the expressions to find the actual JK flip-flop input values and output Z for each possible combination of present states and input
PS
NS
I/P
O/P
(iii) Use the JK flip-flop characteristic table to find the next states (NS), based on the JK flip-flop input vales and the present states (PS).
J | K | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | Qn’

## Slide 11
 |  |  | X=0 |  | X=1 | 
PS |  |  | NS | Z | NS | Z
0 | 0 | 0 | 0 | 0 | 2 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 2 | 2 | 0 | 1 | 1
1 | 1 | 3 | 3 | 1 | 0 | 0
00
10
11
01
1/0
0/1
1/1
0/1
0/0
1/1
0/0
1/0
Since the output depends on the present states and the present input, the sequential circuit is a Mealy machine
State table
State diagram

## Slide 12
Q3. Design a sequential circuit using JK flip-flops and logic gates for the following state diagram.

## Slide 15
Q1 | Q2 | X | Q1+ | Q2+ | Z
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
PS
NS
I/P
O/P
A
B
C
D
0
0
1
0
1
0
0
0
0
1
0
1
1
1
0
1
0
1
0
0
0
0
0
0
Four states are present in the state diagram, so two JK flip-flops are required.
Tabulate the state table with present states (PS) and next states (NS) along with input and output, as shown in the state diagram.

## Slide 16
Q1 | Q2 | X | Q1+ | Q2+ | Z
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
PS
NS
I/P
O/P
A
B
C
D
0
0
1
0
1
0
0
0
0
1
0
1
1
1
0
0
1
0
0
0
0
0
0
J1 | K1 | J2 | K2
Qn | Qn+1 | J | K
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0
1
1
0
Excitation table
1
0
0
1
0
0
1
1
1
0
1
1
1
1
0
1
0
From the present states (PS) and next states (NS) fill out the JK flip-flop inputs using the excitation table for JK flip-flop.
Then use the K maps to find the expressions for the JK flip-flop inputs

## Slide 17
Draw the sequential circuit