## Slide 1
Advance Analog and Mixed Signal Design
Lecture 12
Design Insights of Low-Dropout (Analog & Digital)
Dr. Neeraj Mishra
High Performance Electronics Lab
Electrical & Electronics Eng. Dept.
Birla Institute of Technology & Science Pilani, Pilani Campus

## Slide 2: Introduction to design Insights of LDOs
Low-dropout regulator (LDO) - is a critical building block that generates
  A stable voltage (which can be used as a voltage reference or a supply) irrespective of the external conditions (supply voltage variation, noise etc.).
  An LDO helps in achieving better performance of the internal circuits and usually used together with the bandgap reference to ensure a constant output voltage.

## Slide 3: Cont..

## Slide 4: Cont..

## Slide 5: Principle of operation
The principle of operation of an LDO can be explained as a voltage-controlled voltage source (VCVS). This VCVS is controlled by two voltages
  Reference voltage (Vref)
  feedback voltage (Vfb)
It targeting to maintain a constant voltage (Vout) equal to Vref by supplying sufficient current to the feedback resistance R1​ and load resistance RL​.
reference voltage
feedback voltage
constant voltage
quiescent current
control voltage
error voltage
VCVS
subtraction block
The feedback resistance R1​ defines a minimum current at no-load condition which is called quiescent current (Iq). Elaborating further the control stage of an LDO, we can represent it as a subtraction block, producing the error voltage VE followed by the gain stage, generating the control voltage Vc :

## Slide 6: Cont..
How it work
Subtraction and gain can be implemented using OTA and usually called an error amplifier.
The voltage controlled current source is represented by the MOS transistor and usually called a pass device:
Subtraction and gain
OTA
error amplifier
voltage controlled current source
pass device

## Slide 7: Real LDOs

## Slide 8: Cont..
The difference between
The feedback voltage Vfb​ and the reference voltage Vref produces the control voltage Vc​ which determines current through the pass device,
It ensuring that enough current is supplied to the load resistance RL​ and Vout​ = Vref​ is maintained.
The load capacitance CL​ is playing a vital role during load transients (by supplying extra current) and stability, which will be discussed later.
Subtraction and gain
OTA
error amplifier
voltage controlled current source
pass device

## Slide 9: Practical example of an LDO
Let's have a look on a practical example of an LDO to understand its operation better. The picture below represents a simple LDO with an NMOS pass device and no load.
NMOS pass device
No load

## Slide 10: Cont..

## Slide 11: LDO operation under load

## Slide 12: LDO topologies
LDOs have a variety of topologies and oriented for use with analog or digital circuits. There are two main LDO topologies: NMOS- and PMOS- based.
By architecture:
  With an off-chip load capacitor
  Capacitor-less
By Pass device type:
  NMOS-based
  PMOS-based

## Slide 13: PMOS V/S NMOS LDOs
NMOS-based
PMOS-based

## Slide 14: PMOS V/S NMOS LDOs
A bandgap voltage reference provides a stable reference signal for the regulator.
  An error amplifier (EA), typically implemented as an OTA (Operational Transconductance Amplifier), detects differences between the feedback voltage and the reference voltage, adjusting the pass-element resistance accordingly.
  A feedback resistor network divides the output voltage for comparison with the reference voltage (Vref​). The pass device (usually a MOSFET) regulates resistance between the input and output voltages to maintain stability.
  In practical applications, the pass device is commonly a PMOS transistor. Next, we’ll compare the use of PMOS vs. NMOS topologies:

## Slide 15: PMOS LDOs/NMOS LDOs
PMOS LDOs is the most commonly used topology due to their low dropout voltage, while NMOS pass transistors are practical when the supply voltage is significantly higher than the regulated output.
In an NMOS configuration, the pass transistor acts as a common drain (source follower) with positive gain, whereas the PMOS operates as a common source with negative feedback. This difference requires the op-amp polarity to be adapted accordingly.

## Slide 16: Advantage
The primary advantage of PMOS LDOs is their lower dropout voltage.
The error amplifier output (EAout​) in a PMOS design can swing between GND and Vin​−Vth​, with dropout voltage primarily dependent on Vds​ (around 50mV for saturated devices).
In contrast, NMOS LDOs require the output of the error amplifier to be at least Vth​ above the output voltage to turn on the pass transistor.
This means the output voltage is inherently limited to at least Vth below the input voltage, with additional margin for loop regulation.
Furthermore, NMOS pass devices are typically high-power or high-voltage transistors designed to handle significant current and voltage, and their threshold voltage is often higher than the standard 1V of regular transistors.

## Slide 17: Single Stage OTAs

## Slide 19: 2 Stage or Millar OTAs

## Slide 20: Folded Cascode OTAs

## Slide 21: Telescopic OP AMP/OTAs

## Slide 22: Comparison

## Slide 23: Feedback resistance calculation
The reference voltage is usually provided by the bandgap reference and usually outputs a fixed voltage, that might be different from what we want to see at the output of LDO. Solution to this is to use a voltage divider in the feedback of the LDO:

## Slide 24: Cont..

## Slide 25: Cont..

## Slide 26: Output voltage error
There are 3 main sources of the output error in LDO:
Voltage divider mismatch
  (R1​ and R2​)
  Gain error of error amplifier
  Reference voltage error

## Slide 27: 1. Voltage divider mismatch
The resistor value variation in CMOS process in generally big and can be up to 15-30%, depending on the resistor type.
Since only the ratio between R1​ and R2​ matters (and not their absolute values), we can neglect the error, introduced by the divider if we match them in layout.

## Slide 28: 2 Gain error of error amplifier

## Slide 29: Cont..

## Slide 30: 3 Reference voltage error

## Slide 31: Calculation Example

## Slide 32: Cont..

## Slide 33: Feedback Resistor Highlights
Use low-mismatch resistors, such as polysilicon resistors;
Make resistors as wide as possible to reduce mismatch;
Use unit-sized segments; connect resistors in parallel or in series, if needed;
Match feedback resistors in layout;
Total resistance defines quiescent current (Iq​) - a trade-off between stability and power consumption;

## Slide 34: Stability & Transfer Function
As any feedback system, the LDO is a subject to stability analysis.
Let's dive into a typical LDO structure and understand the location and role of the poles and zeros.
In a typical LDO there are two main poles.

## Slide 35: Cont..

## Slide 36: Cont..

## Slide 37: Transfer function of the LDO

## Slide 38: Compensation
In the previous chapter we saw that the load pole ωp2​ moves, when the load is changing. This effect lead to change in phase margin, which can lead to unstable condition (oscillations). There are two main ways to compensate this effect:
  Zero insertion
  Cgs​ shielding through buffer

## Slide 39: Using a ESR zero
One of the ways to compensate our LDO with external capacitor is to utilize the capacitor's equivalent series resistance (ESR). Every capacitor model contains the series resistance that represents the losses in the capacitor.

## Slide 40: Cont..

## Slide 41: Using a buffer
Another way to compensate an LDO is to add a buffer between the output of the amplifier and the pass device. Effectively, adding a buffer will shield the output of the error amplifier from the large Cgs​ of the pass device

## Slide 42: Cont..

## Slide 43: LDO Parasitics
In the design of LDO with an off-chip capacitor, it's very important to take into account parasitics, associated with the output node. The main contributors are I/O pads, bondwires, packaging and PCB trace:

## Slide 44: LDO Parasitics
Let's now have a detailed look into these contributors.
  The I/O pad is a large piece of metal so its contribution is mostly capacitive. The typical capacitance for the analog I/O pad is around 1-2pF and usually mentioned in the process documentation.
  The next piece is the bondwire - metal interconnect between the chip and package. Bondwires are typically made of gold to achieve low resistance (≈50mΩ/mm).
  However, due to relatively big length, the bondwire brings a significant inductance to the picture (≈1nH/mm) and it has to be taken into account.

## Slide 45: Cont..

## Slide 46: Digital LDO
Digital control, sandwiched by ADC and DAC
ADC: analog to digital converter, DAC: digital to analog converter
Vin
Vout
A
Vin
Control
V
ref
ADC
DAC = power-FET
Vg
ADC
control
Analog circuit-based feedback
V
ref
Rload
Vg[n-1:0]
Vout
Rload
Cout
Cout

## Slide 47: Digital LDO
A digital LDO replaces the traditional analog feedback loop with a digital feedback loop.
The idea: use digital control hardware as the controller, surrounded by:
  An ADC (to sense the voltage difference).
  A DAC implemented as a power-FET array (to regulate the output).
Operation flow:
  The ADC measures the difference between the reference voltage and the output voltage.
  It generates an error code proportional to this difference.
  The digital controller processes this error code and produces a digital output VgV_gVg​.
  Each bit of VgV_gVg​ drives one power transistor in the FET array, turning it ON or OFF.
  By adjusting how many FETs conduct, the effective resistance of the array changes, thereby regulating the output voltage toward the reference.
Similar to the analog case, a Cout capacitor is still required since the feedback speed of the digital LDO is not infinite.

## Slide 48: Analog vs Digital LDOs
Analog LDO
Pros
  High bandwidth for fast transient response
  High power supply rejection ratio (PSRR)
  Small output ripple
Cons
  Complex/bulky analog design
  Limited scalability to low voltage
  Loop gain depends on operating voltage
Digital LDO
Pros
No major analog components and synthesizable control
Scales well for low-voltage operation
Decouples loop gain from operating voltage
Cons
Low bandwidth
Low PSRR
Large output ripple

## Slide 49: Analog v/s Digital LDOs
Analog LDO – Advantages:
  High bandwidth → enables fast transient response.
  High PSRR (Power Supply Rejection Ratio) → effective noise suppression.
  Low output ripple → cleaner regulated voltage.
Analog LDO – Limitations:
  Requires bulky and complex analog circuit design.
  Scalability issues at low supply voltages.
  Loop gain depends on the input operating voltage.
Digital LDO – Advantages:
  No major analog components → fully synthesizable digital control.
  Well-suited for low supply voltage operation.
  Loop gain is independent of the input operating voltage.
Digital LDO – Limitations:
  Low bandwidth → slower transient response.
  Poorer PSRR compared to analog.
  Larger output ripple.

## Slide 50: Input Voltage
Limited Vin scalability
Typically, Vin > 0.6-0.7V
A high-speed OP amplifier
Better Vin scalability
0.5V or less
Vin
Vout
A
Vin
Control
V
ref
ADC
Vg
V
ref
Rload
Vg[n-1:0]
Vout
Rload
Cout
Cout
Analog LDO
Digital LDO
Analog LDO:
The input voltage feeds both the power FET and the analog amplifier.
If the input voltage is too low, designing a high-performance amplifier becomes very difficult.
As a result, the minimum input voltage for analog LDOs is typically 0.6–0.7 V, and in some cases up to ~1 V.
Since the amplifier must also be high bandwidth, achieving this under low supply voltage is even more challenging.
· Digital LDO:
Contains no major analog components, so it is not constrained by amplifier design.
This gives better scalability with input voltage.
Digital LDOs can typically operate with input voltages as low as 0.5 V or even less.

## Slide 51: Power-FET’s Source-Gate Voltage (Vsg)
Vsg=Vin-Vg between Vin-Vth and 0V
i.e., Vg is analog voltage
Vsg=Vin-Vg: either 0V or Vin
i.e., Vg is digital voltage
Vin
Vout
A
Vin
Control
V
ref
ADC
Vg
V
ref
Rload
Vg[n-1:0]
Vout
Rload
Cout
Cout
Analog LDO
Digital LDO

## Slide 52: Deep Dive

## Slide 53: Output Voltage
Vout = Vin–0.2V to ~0V
Power FET is typically in saturation
If a load needs Vin-0.1V, we supply Vin
Vout = Vin–0.05V to ~0V
Power FET is in linear to saturation
Wider output voltage range
0.05V~
0.2V~
Vin
Vout
A
Vin
Control
V
ref
ADC
Vg
V
ref
Rload
Vg[n-1:0]
Vout
Rload
Cout
Cout
Analog LDO
Digital LDO

## Slide 54: Output Voltage Range – Analog vs. Digital LDO

## Slide 55: Dropout Voltage Requirement
DLDO
ALDO
Vin set to the highest VDD requirement
An LDO can be bypassed
ALDO
0.4V
Core
0.6V
Core
0.2V
Vin=0.6V
0.5V
Core
DLDO
DLDO
0.4V
Core
0.5V
Core
0.6V
Core
0.2V
0.1V
ALDO
Less dropout voltage requirement
Support wider output voltage
Vin=0.6V

## Slide 56: Implication of Output Voltage Range in SoC Usage
Consider an SoC with three cores requiring:
  Core 1: 0.6 V
  Core 2: 0.5 V
  Core 3: 0.4 V
The input supply is set to the highest requirement, e.g. 0.6 V.
Analog LDO Case
Core 1 (0.6 V): Supplied directly from the input (no LDO needed).
Core 2 (0.5 V):
  Needs 100 mV lower than input.
  Analog LDO typically requires ~200 mV drop across the power FET (saturation).
  Therefore, it cannot regulate down to 0.5 V → must use 0.6 V directly.
  This results in power waste for this core.
Core 3 (0.4 V):
  Within the analog LDO regulation range.
  Can be supplied by an analog LDO.
Digital LDO Case
Core 1 (0.6 V): Direct supply.
Core 2 (0.5 V):
  Digital LDO has a much smaller required source-to-drain drop (~50 mV).
  Therefore, it can regulate from 0.6 V down to 0.5 V.
  Provides a better supply voltage match compared to analog LDO.
Core 3 (0.4 V): Also supported by digital LDO.

## Slide 57: Key Specifications
Silicon area
Input, reference, and output voltage (Vin, Vref, Vout)
Edge time (tedge)
Voltage droop and overshoot (Vdroop, Vovershoot)
Response and settling time (tresponse, tsettle)
Load, quiescent, power-FET, and capacitor current (Iload, Iq, Ipwr, Icap)
Peak current and power efficiency (CEpeak, PEpeak)
Dropout voltage (Vdropout)
Power supply rejection ratio (PSRR)
Load regulation performance FoMs: ps FoM and pF FoM
Maximum and minimum load current (Iload,max, Iload,min)
DAC and ADC number of bits (NDAC,NADC)
Dead-zone voltage (Vdz)
DAC step size (VDAC,ss)
IR drop voltage (VIR)

## Slide 58: Silicon Area
Active components scale better than passive with technology scaling
Vin
ctrl
Vref
Vout
ADC
17.5%
9.6%
4.8%
68.1%
Output capacitor (100 pF)
Digital controller
65-nm example [Kim-VLSI19]
ADC
Power FETs
Rload
g
V [n-1:0]
Cout
· Why important?
In digital LDOs, silicon area is a critical factor since multiple LDOs are often integrated on a single chip.
· Area Breakdown (from recent publication):
Output capacitor → dominates, accounting for ~70% of the total area.
The remaining area is shared among:
  ADCs
  Digital controllers
  Power FETs
· Key Insight:
With technology scaling, active components (transistors, controllers, ADCs) shrink significantly.
Passive components (like capacitors) do not scale as effectively.
Thus, the output capacitor remains the major contributor to silicon area.

## Slide 59: Voltage Droop (Vdroop)
Vout’s maximum downward
deviation from Vref
Vdroop is typically targeted to less than 10% of Vout
ΔIload,max can be different from Iload,max
Time
Iload
Vdroop
Time
Vout
ΔIload,max

## Slide 60: Edge Time (tedge)
edge
t is a function of the
clock period of a load
1 GHz core  1-ns tedge
2 GHz core  0.5-ns tedge
Iload
Vdroop
Time
Vout
tedge
ΔIload,max
Time

## Slide 61: Response Time (tresponse)
It is roughly proportional to feedback latency
In synchronous control, it is proportional to tclk
In asynchronous control, it is proportional to circuit latency/delay
Time
Iload
Time
Vout
tresponse
ΔIload,max

## Slide 62: Settling Time (tsettle)
Time
Iload
tsettle
Time
Vout
1 LSB
Time to take for Vout to settle within less than a small % of Vref (e.g., +/- 0.5%)
The output can have a ripple
ΔIload,max

## Slide 63: Voltage Overshoot (Vovershoot)
Time
Iload
V
overshoot
Time
Vout
Vout’s maximum upward
deviation from Vref
Vovershoot is typically targeted to less than 10% of Vout
ΔIload,max is different from Iload,max
ΔIload,max

## Slide 64: Current and Power Efficiency (CE, PE)
Vin
ctrl
V
ref
Vout
ADC
𝑃𝐸 =
𝑉𝑜𝑢𝑡 .𝐼𝑙𝑜𝑎𝑑
𝑉𝑖𝑛 ( 𝐼𝑞 + 𝐼𝑙𝑜𝑎𝑑)
𝑉𝑜𝑢𝑡
≈
𝑉𝑖𝑛
𝐼𝑙𝑜𝑎𝑑
𝑞
𝐶𝐸 =
𝐼 + 𝐼
𝑙𝑜𝑎𝑑
q
If: I << I
load
Iq
Ipwr
f
s
Quiescent current
Rload
Load current;
Equal to Ipwr in the steady state
Total current
Vg
Cout
Power FET current
Iload
Icap
Capacitor current
~0 in the steady state

## Slide 66: Current Efficiency vs. Peak Current Efficiency
99.9% CEpeak
99.999% CEpeak
 1% or less loss for Iload = 0.1∙Iload,max to Iload,max
 1% or less loss for Iload = 0.001∙Iload,max to Iload,max
load
log(I )
CE
1 |  | 1 |  | 1 |  | 1
10,000 |  | 1000 |  | 100 |  | 10
1
CEpeak=99.9%
99.99%
99.999%
𝐶𝐸 =
𝐼𝑙𝑜𝑎𝑑
𝐼𝑞 + 𝐼𝑙𝑜𝑎𝑑
𝐶𝐸𝑝𝑒𝑎𝑘 =
𝐼
𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝐼𝑞 + 𝐼𝑙𝑜𝑎𝑑,𝑚𝑎𝑥

## Slide 67: Cont..

## Slide 68: Dropout Voltage (Vdropout)
Vin
ctrl
V
ref
Vout
ADC
𝑃𝐸 =
𝑉𝑜𝑢𝑡 𝐼𝑙𝑜𝑎𝑑
𝑉𝑖𝑛 (𝐼𝑞 + 𝐼𝑙𝑜𝑎𝑑)
𝑉𝑜𝑢𝑡
≈
𝑉𝑖𝑛
𝑉𝑖𝑛 − 𝑉𝑑𝑟𝑜𝑝𝑜𝑢𝑡 𝑉𝑑𝑟𝑜𝑝𝑜𝑢𝑡
= = 1 −
𝑉 𝑉
𝑖𝑛 𝑖𝑛
The larger dropout voltage, the lower PE
Iq
Iload
Vdropout
𝐼𝑙𝑜𝑎𝑑
𝑞
𝐶𝐸 =
𝐼 + 𝐼
𝑙𝑜𝑎𝑑
Vg
R
load
C
out

## Slide 69: Power Supply Rejection Ratio (PSRR)
Hz
PSRR
Active Feedback
output capacitor
∆𝑉𝑜𝑢𝑡
𝑃𝑆𝑅𝑅 = 20 log
∆𝑉𝑖𝑛
[𝑑𝐵]

## Slide 70: ps Figure of Merit (ps-FoM)
Pseudo current efficiency
Dynamic load regulation performance
This FoM aims to capture the product of the LDO response time and current efficiency
Smaller is better
𝑝𝑠 𝐹𝑜𝑀 = 𝑡
𝑟𝑒𝑠𝑝𝑜𝑛𝑠𝑒
𝐶𝑜𝑢𝑡 . ∆𝑉𝑜𝑢𝑡
∆𝐼
𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
∙
𝐼𝑞
∆𝐼
𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
[Hazucha-JSSC05]
Pseudo response time

## Slide 71: Caveats for the ps-FoM

Vin, tedge, and ΔIload,max have a strong impact on FoM.
ps FoM favors large ΔIload,max
(∵ 𝑝𝑠 𝐹𝑜𝑀 ∝ Δ𝑉𝑜𝑢𝑡/Δ𝐼2 )
𝑙𝑜𝑎𝑑,𝑚𝑎𝑥
Using a large output capacitor and proportionally increasing ΔIload,max improves ps FoM in a same design

Note ΔIload,max, not Iload,max
Ideal to compare designs having similar Vin, tedge, and ΔIload,max
0 2 4 6 8 10 12 14 16 18 20 22 24 26 28 30
300
275
250
225
200
175
150
125
100
75
50
IN
V = 1V
VIN= 0.5V
IN
V = 1V
IN
V = 0.5V
VIN=1V, ILOAD=407.7mA
VIN=0.5V, ILOAD=91.8mA
TEDGE [ns]
VDROOP [mV]
* measurement Dropout=10%  VIN
0
1
2
3
FOM (in Table I) [ps]
[Kim-VLSI19]

## Slide 72: pF Figure of Merit (pF-FoM)
Normalized voltage droop
Alternative FoM for dynamic load regulation performance
How small the voltage droop is at the power (Iq) and area cost (Cout)
Smaller is better
pF FoM works better to compare LDOs with different ΔIload,max
Should use it for designs having similar Vin and tedge
[Kim-JSSC17]
𝑝𝐹 𝐹𝑜𝑀 = 𝐼
𝑞
∆𝑉𝑜𝑢𝑡
∆𝐼
𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑉𝑜𝑢𝑡
𝐶
𝑜𝑢𝑡

## Slide 73: Maximum Load Current (Iload,max)
𝑃𝑜𝑤𝑒𝑟 𝐹𝐸𝑇 𝑢𝑛𝑖𝑡 𝑐𝑢𝑟𝑟𝑒𝑛𝑡 = 𝐼
𝑢
If power FETs are sized in the power of 2
𝑀𝑎𝑥𝑖𝑚𝑢𝑚 𝑙𝑜𝑎𝑑 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥

## Slide 74: DAC Number of Bits (NDAC)
𝑀𝑎𝑥𝑖𝑚𝑢𝑚 𝑙𝑜𝑎𝑑 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑃𝑜𝑤𝑒𝑟 𝐹𝐸𝑇 𝑢𝑛𝑖𝑡 𝑐𝑢𝑟𝑟𝑒𝑛𝑡 = 𝐼
𝑢
If power FETs are sized in the power of 2
𝑁𝐷𝐴𝐶 = log2(
𝐼
𝑢
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥 + 1)
𝐼
𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑢
= 𝐼 (2𝑁𝐷AC − 1)

## Slide 75: DAC Step Size (VDAC,SS)
𝑉𝐷𝐴𝐶, 𝑆𝑆 = 𝐼𝑢 .𝑅𝑙𝑜𝑎𝑑,𝑚𝑎𝑥
𝑃𝑜𝑤𝑒𝑟 𝐹𝐸𝑇 𝑢𝑛𝑖𝑡 𝑐𝑢𝑟𝑟𝑒𝑛𝑡 = 𝐼
𝑢
Output voltage resolution (worst-case)
If power FETs are sized in the power of 2
𝑀𝑎𝑥𝑖𝑚𝑢𝑚 𝑙𝑜𝑎𝑑 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑁𝐷𝐴𝐶 = log2(
𝐼
𝑢
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥 + 1)
𝐼
𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑢
= 𝐼 (2𝑁𝐷AC − 1)

## Slide 76: Minimum Load Current (Iload,min)
𝑢
= 𝐼 .
𝑉𝑜𝑢𝑡
𝐼𝑙𝑜𝑎𝑑,𝑚𝑖𝑛
𝑢
= 𝐼 .
𝑉𝑜𝑢𝑡
1/
𝐼
𝑟 𝑢
= 𝑟 .𝑉
𝑜𝑢𝑡
r=0.01 if targeting VDAC,SS=1% of Vout
𝑉𝐷𝐴𝐶, 𝑆𝑆 = 𝐼𝑢 .𝑅𝑙𝑜𝑎𝑑,𝑚𝑎𝑥
𝑃𝑜𝑤𝑒𝑟 𝐹𝐸𝑇 𝑢𝑛𝑖𝑡 𝑐𝑢𝑟𝑟𝑒𝑛𝑡 = 𝐼
𝑢
Output voltage resolution (worst-case)
If power FETs are sized in the power of 2
𝑀𝑎𝑥𝑖𝑚𝑢𝑚 𝑙𝑜𝑎𝑑 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑁𝐷𝐴𝐶 = log2(
𝐼
𝑢
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥 + 1)
𝐼
𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑢
= 𝐼 (2𝑁𝐷AC − 1)

## Slide 77: Minimum Load Current (Iload,min)
𝐼
𝑙𝑜𝑎𝑑,𝑚𝑖𝑛
𝑢
= 𝐼 .
𝑉𝑜𝑢𝑡
𝑉𝐷𝐴𝐶,𝑆𝑆
𝑢
= 𝐼 .
𝑉𝑜𝑢𝑡
𝐼
𝑢
𝑟 . . 𝑉𝑜𝑢𝑡 𝑟
= ≫ 𝐼
𝑢
e.g., I
load,min
=100·I
u
for r=0.01
𝑢
= 𝐼 .
𝑉𝑜𝑢𝑡
𝐼𝑙𝑜𝑎𝑑,𝑚𝑖𝑛
𝑢
= 𝐼 .
𝑉𝑜𝑢𝑡
1/
𝐼
𝑟 𝑢
= 𝑟 .𝑉
𝑜𝑢𝑡
r=0.01 if targeting VDAC,SS=1% of Vout
𝑉𝐷𝐴𝐶, 𝑆𝑆 = 𝐼𝑢 .𝑅𝑙𝑜𝑎𝑑,𝑚𝑎𝑥
𝑃𝑜𝑤𝑒𝑟 𝐹𝐸𝑇 𝑢𝑛𝑖𝑡 𝑐𝑢𝑟𝑟𝑒𝑛𝑡 = 𝐼
𝑢
Output voltage resolution (worst-case)
If power FETs are sized in the power of 2
𝑀𝑎𝑥𝑖𝑚𝑢𝑚 𝑙𝑜𝑎𝑑 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑁𝐷𝐴𝐶 = log2(
𝐼
𝑢
𝐼𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥 + 1)
𝐼
𝑙𝑜𝑎𝑑, 𝑚𝑎𝑥
𝑢
= 𝐼 (2𝑁𝐷AC − 1)

## Slide 78: Clock Frequency (fclk)
Clock for a synchronous ADC and a controller
High clock frequency (fclk) improves tresponse, tsettle, Vdroop, and Vovershoot
High fclk increases Iq, thus degrading CE
Vin
Vref
Vout
Rload
Clk
Clk
Vg
Cout
ctrl
ADC

## Slide 79: Output Ripple Size (Vripple)
High fclk increases Vripple
Because a controller makes a correction before the previous correction is fully applied on a load [Nasir-TPE16]
Vripple
I𝑙𝑜𝑎𝑑 ,𝑚𝑖𝑛
≅ α ∙ Iu ∙ Rload , , where α = 1 for fclk ≪ V
C
out out
Vin
Vref
V
out
R
load
Clk
Clk
The controller output alternates between two codes with 1 LSB difference
Vg
Cout
ctrl
ADC

## Slide 80: Output Ripple Size (Vripple)
Vripple is also a function of
temperature &
Iload
Worst-case Vripple
@ Iload,min and high temperature
10
15
20
25
80C
Vripple
[mV]
=1, IU=6nA, 11-bit power-FET array
*Simulation
Vin=0.55V, Vout=0.45V
24C
5
0C
0
100 1,000 10,000
Iload [nA]
Source: S.J. Kim (Columbia)
Vripple
I𝑙𝑜𝑎𝑑 ,𝑚𝑖𝑛
≅ α ∙ Iu ∙ Rload , , where α = 1 for fclk ≪ V
C
out out

## Slide 81: IR Drop (VIR)
Parasitic resistance (Rpara) can make Vout ≠ Vout,far
The ADC senses Vout, not Vout,far
This deviation, VIR, grows with Iload
Vin
Ctrl
Vref
Vout
ADC
Iload
Rpara Vout,far
Time
Iload
V
IR
Time
Vout
𝑉𝐼𝑅 = 𝑅𝑝𝑎𝑟𝑎 � 𝐼𝑙𝑜𝑎𝑑
Rload
C
out