## Slide 1
Advance Analog and Mixed Signal Design
Lecture 7
Amplifier Stability
Dr. Neeraj Mishra
High Performance Electronics Lab
Electrical & Electronics Eng. Dept.
Birla Institute of Technology & Science Pilani, Pilani Campus

## Slide 2: Motivation
Operational amplifiers are a universal building block and most analog designers will design one
An oscillating amplifier is a designer’s nightmare and leads to revisions. Gain peaking or settling tails can be detrimental to system performance
From practice, more time is spent on assuring the amplifier’s stability under all conditions than on other features
Return of Investment (ROI): time saved > time spent

## Slide 3: Stability
We will focus primarily on small signal stability, touch upon large signal (conditional) stability. We will not cover stability over temperature or time.
Definition of stability
1 : the quality, state or degree of being stable:
the strength to stand or endure
the property of a body that causes it when disturbed from a condition of equilibrium or steady motion to develop forces or moments that restore the original condition
resistance to chemical change or physical disintegration
time
voltage

## Slide 4: Benefits and Challenges
There are over 15000 commercially available operational amplifiers and much more integrated inside mixed-signal ICs
Variety is due to the many different optimization objectives
They must be robust in variety of operating conditions and feedback variations
For optimum performance one must trade-off conflicting requirements
Poor compensation leads in worse case to system failure and in best case to wasted power and area
Concepts are applicable to other circuits (i.e. regulators, references, etc.)
Speed
Speed
Speed
Accuracy
Voltage
Power
Accuracy
Power

## Slide 5: Stable (enough?)
Stability requires power, die area, complexity and time investments
Depends on operating conditions, load and system configuration
Impact key amplifier parameters such as speed, power, settling time but difficult to benchmark
time
Vout
𝐹𝑂𝑀:
𝐺𝐵𝖶 G 𝐺𝐵𝖶 G 𝐺𝐵𝖶·𝐶𝐿𝐷 G 𝐺𝐵𝖶·𝐶𝐿𝐷·𝜑𝑀
𝐼Q 𝐼Q·𝑉𝐶𝐶 𝐼Q·𝑉𝐶𝐶 𝐼Q·𝑉𝐶𝐶

## Slide 6: Outline
Introduction and background
Refresher on feedback theory, bode plots and gain and phase margin
Amplifier frequency response
Basic compensation techniques
Alternative (advanced) compensation schemes
Practical tips and suggestions

## Slide 7: Outline
Introduction and background
Refresher on feedback theory, bode plots and gain and phase margin
Amplifier frequency response
Basic compensation techniques
Alternative (advanced) compensation schemes
Practical tips and suggestions
Feedback theory Poles, zeros Bode plots Stability criterion

## Slide 8: Ideal Amplifier
Integrated amplifiers can have large gain (80-140dB), but it is very process, temperature, supply dependent
Need feedback to eliminate these dependencies. Passive feedback elements such as resistors offer better stability and linearity
Many amplifier parameters will be controlled by local feedback loops and therefore amplifiers are interacting multi-loop systems
Vin
Vout
Rf
Rin

## Slide 9: Feedback Concept
Compare the input signal to a sensed copy of the output
The difference (error) is amplified
The output is driven to the desired amplitude
The accuracy now mainly determined by the feedback network
Aβ
Aβ: Loop Gain (T)
Return Ratio)
A: Open Loop Gain
Output
Input
CL
β: Feedback Factor
1/β : ~ Closed Loop Gain (A )

## Slide 10: Feedback Concept
𝐺𝑎𝑖𝑛 =
𝐴
=
1/𝛽
1 + 𝐴𝛽 1 + 1/𝐴𝛽
Negative Feedback
  Increases accuracy (with accurate β)
  Reduces sensitivity to gain variations
  Linearizes system
  Improves input/output impedance
  Provides more usable bandwidth
However
Lowers achievable gain
Increases area and complexity
Can lead to instability
Output
Input
𝑖𝑛𝐹𝐵
𝑖𝑛
𝑅 = 𝑅 (1 + 𝐴𝛽)
𝑅𝑜𝑢𝑡𝐹𝐵 =
𝑅𝑜𝑢𝑡
(1 + 𝐴𝛽)
For voltage (series-shunt) feedback:

## Slide 11: Frequency Dependence
The open loop gain (A) and feedback factor (β) do not stay constant over frequency
Feedback loop has to be analyzed over frequency
𝑉
𝑉𝑖𝑛𝑝𝑢𝑡
𝐶𝐿 𝐺𝑎𝑖𝑛 = 𝑜𝑢𝑡𝑝𝑢𝑡 =
1
𝛽(𝑗𝜔)
1 +
1
𝐴(𝑗𝜔)𝛽(𝑗𝜔)
𝑇(𝑗𝜔) = 𝐴(𝑗𝜔)𝛽(𝑗𝜔)
𝜔[𝑟𝑎𝑑/𝑠] = 2𝜋𝑓[𝐻𝑧]
Output
Input
A(j)
β(j)
amplitude
phase delay

## Slide 12: Negative and Positive Feedback
With too much delay in the signal fed back (phase shift) in the system the negative feedback can become positive leading to increasing output and therefore instability.
Negative Feedback
Positive Feedback
+ delay

## Slide 13: Feedback Stability: Nyquist Stability Criterion
Stable
Unstable
Re Re
The Nyquist plot is obtained by tracing in the complex plane the magnitude and phase of the loopgain T(j) from =0 to =j∞
Based on Nyquist Stability Criteria (1932) for a feedback amplifier (without right half plane poles) a necessary and sufficient condition for stability is that the Nyquist plot in the T(j) plane of the loopgain T(j) does not encircle the
-1+j0 (180) [1,17]
Im Im
=∞ =∞
-1 -1
T(j𝜔) = 𝐴
0
j𝜔 j𝜔 =0 =0
1 + 𝜔𝑧1 1 + 𝜔𝑧2 …
1 + j𝜔
𝜔𝑝1
1 + j𝜔
𝜔𝑝2
…

## Slide 14: A practical simplification
|T| at f180 < 1
|T| at f180 > 1
For most practical feedback amplifier cases we aim to assure that the frequency where the phase is inverted (-180) the magnitude of the loopgain is attenuated (below 1=0dB)
Im
Re
GM
M-1

## Slide 15: Bode Plots: Refresher
A graphical method to represent the small signal frequency response of a system at a particular operating point
Useful to understand trends for stability by looking at gain or loopgain magnitude and phase
Always follow up by transient simulations and disturbances!
T(j𝜔) = 𝐴0
1 + j𝜔
𝜔𝑧1
1 + j𝜔
𝜔𝑧2
…
1 + j𝜔
𝜔𝑝1
1 + j𝜔
𝜔𝑝2
…
|𝐓| = 20𝑙𝑜𝑔10|𝑇 𝑗𝜔 |
𝐓 =  𝑡𝑎𝑛−1
𝜔
𝜔𝑧1,2..
−  𝑡𝑎𝑛−1
𝜔
𝜔𝑝1,2..
𝜔[𝑟𝑎𝑑/𝑠] = 2𝜋𝑓[𝐻𝑧]

## Slide 16: Bode Plots: LHP Pole and Zero
-3dB at fp
-20dB/dec
-45 at fp
-90
0
-45/dec
+20dB/dec
+3dB at fz
90
45 at fz
+45/dec 0
Bode Plot: LHP Pole Bode Plot: LHP Zero

## Slide 17: Gain and Phase Margin
From Nyquist Criterion the degree of a system’s stability can be quantified by:
Phase Margin (M): The phase at the frequency where the loopgain
(T) is 0dB (referenced to -180°)
Gain Margin (GM): The attenuation where the phase of the loopgain
(T) has reached 180°
M=22
GM=20dB

## Slide 18: Op amp Feedback Stability: Graphical Method
Loopgain T = Aβ
Log(T) = Log(A) + Log(β)
Log (T) = Log(A) – Log(1/β)
Use above equation in a plot:
Separately plot 20Log(A) and 20Log(1/β)
Loopgain is difference of curves, unity gain is where lines cross
For stability loopgain needs to cross unity with 20dB /decade roll-off
Vin
Vout
R2
R1
β
19

## Slide 19: Op amp Feedback Stability: Graphical Method
rD = 1/gm of QD (current dependent) CD = parasitic diode capacitance
CD
rD
QD
CIN
𝑧
𝑓 =
1
2𝜋𝑟𝐷(𝐶𝐷 + 𝐶𝐼𝑁)
𝑝
𝑓 =
1
2𝜋𝑟𝐷𝐶𝐷
stable
unstable
A
stable
1/

## Slide 20: Op amp Feedback: Conditional Stability
Stable if feedback network is restricted to certain values
  Unstable with CL gain > 20 (26dB)
  Stable with CL gain < 20 (26dB)
Much improved power efficiency
Careful in any condition that can lead to loss of open loop gain!
A
1/β
1/β
-40dB/dec.
-20dB/dec.
M=0
M=90

## Slide 21: Bode Plots: LHP vs RHP Pole and Zero
Pole magnitude decreases with frequency, zero increases with frequency
LHP pole or RHP zero phase decreases with frequency
  RHP zero reduces phase margin!
  Commonly found in circuits (i.e. Miller capacitance feed-forward)
RHP pole or LHP zero phase increases with frequency
  RHPP lead to system instability
  Not known [?] in amplifiers
time
voltage

## Slide 22: Relating to Transient Response [19]
Time to phase shift
TS: time shift from input to output signal TP: period of signal
: phase shift of the signal from input to output
To calculate phase shift in degrees:
𝑇𝑃
𝜃 = 𝑇𝑆 · 360° =
0.225𝑚𝑠
1𝑚𝑠
· 360° = 81°
TS=0.225ms
TP=1ms
Time(ms)
Vin
Vf

## Slide 23: Relating to Transient Response [19]
Dominant (2 pole) system responses
Small-step overshoot AC Response vs. Frequency

## Slide 24: Outline
Introduction and background
Refresher on feedback theory, bode plots and gain and phase margin
Amplifier frequency response
Basic compensation techniques
Alternative (advanced) compensation schemes
Practical tips and suggestions
Causes of poles and zeros Number of gain stages

## Slide 25: Trends to Remember
100KΩ
10pF
vx
Zld 5KΩ
2pF
|vx/vin|
Zld:
2pF 5K&10pF
(5K&10pF)||2pF
Vin

## Slide 26: Frequency response of an amplifier[20]
Parasitic capacitances as well as multiple gain paths introduce poles and zeros in the frequency response.
CGS
CSB
RS
RL
CGD VOUT CGD
VIN

## Slide 27: Frequency compensation
Introduces elements in the feedforward or feedback path to ensure needed phase and gain margin for stability
Reduces dependency on parasitic elements and their variation over process/temperature/supply in the circuit
Always comes with reduction of power to bandwidth ratio
p1
p2
Figure [20]

## Slide 28: Amplifiers: Number of stages
1 Stage Amplifiers
  Simplicity, stability and power efficiency (++)
  Low gain, high output impedance, limited output range, load sensitivity, limited current drive capability (––)
2 Stage Amplifiers
  Lower output impedance, output range, load insensitivity, input and output ranges decoupled, current drive capability (++)
  Simplicity, cap load drive, settling time, power efficiency (+)
  Limited gain, higher offset and noise, distortion, current drive capability (bipolar amplifiers) (–)
3 Stage Amplifiers
  High gain, lower offset and noise, less distortion, current drive capability (bipolar amplifiers) (++)
  Complexity, power efficiency, large and small signal stability concerns (––)

## Slide 29: What is a gain stage in the signal path?
Gain stages:
  common source
  common gate if Zin << ZL
  differential stage
Not gain stages:
common drain (follower)
common gate if Zin > ZL
V
IN
R
VOUT
LD
RLD
VOUT
RIN
VIN
V
IN
V
OUT
RLD
V
OUT
V
IN
RLD
RLD
RLD VOUT
VIN
VIN

## Slide 30: More stages  lower achievable bandwidth
Log Freq.
|A|
Log Freq.
|A|
-60dB/dec
-40dB/dec
-20dB/dec
G1
G
3
C
M1
Cm2 G2
V
IN
G1
G
2
G1
C
M1
CLD
R0 C0
R0 C0
R0
CLD
R0 C0
R0
VIN
R0 CLD
V
IN

## Slide 31: Outline
Introduction and background
Refresher on feedback theory, bode plots and gain and phase margin
Amplifier frequency response
Basic compensation techniques
Alternative (advanced) compensation schemes
Practical tips and suggestions
compensation techniques 2 stage amplifier example

## Slide 32: Types of compensation
Load Compensation – the load capacitor provides compensation
Shunt Compensation – a (large) capacitor to kill gain of a stage
Parallel (Lead) Compensation – additional RC in gain path to cancel out pole introduced by load
Miller Compensation – using a capacitor across a high gain stage to provide the dominant pole in the frequency response. This has many variants
Feed-forward Compensation – using a faster (lower gain) element or stage to bypass high gain stages particular frequencies
Countless combination of the above ….

## Slide 33: Load compensation (single stage amplifier)
Large load capacitors simply reduce Gain-Bandwidth but the Phase Margin still 90° Stable but limited gain and output impedance is high.
𝑣
𝑚 out
𝐴 = 𝐺 𝑍 ≅
𝐺𝑚𝑅𝑙𝑑
1+jω/ω𝑐
VIN
VOUT
CLD
ZOUT
|A|
Freq
C
LD
Single pole
-20dB/dec
𝐶
𝜔 =
𝐺
𝑚
𝐶𝐿𝐷

## Slide 34: Two stage amplifier: Frequency response
1
𝑝 =
1
𝑅𝐸Q𝐶𝐸Q
2
𝑝 =
1
𝑅𝐿𝐷𝐶𝐿𝐷
0
𝐴 = 𝑔𝑚 𝑔𝑚 𝑅 𝑅
𝑖 𝑜 𝐸Q 𝐿𝐷
Cross over frequency
p
3
VIN-
VOUT
CEQ
VIN+
CLD
RLD
RIN CIN
REQ CEQ
gmi
gmo
V
IN
VOUT RLD CLD
M=0°

## Slide 35: Two stage amplifier: Shunt compensation
CC=5nF
CC=1pF
Not practical for ICs.
VIN-
C
C
VIN+
CLD RLD
VOUT
M=45°
M=0°

## Slide 36: Parallel (lead) compensation [3]
Select RCCC = RLDCLD
Original poles (w/o comp):
1
𝑝 =
1
𝑅𝐸Q𝐶𝐸Q
2
𝑝 =
1
𝑅𝐿𝐷𝐶𝐿𝐷
Compensated poles/zeros:
1
𝑝 =
1
𝑅𝐸Q𝐶𝐶
2
𝑝 =
1
𝑅𝐶𝐶𝐸Q
1
𝑧 =
1
𝑅𝐸Q𝐶𝐸Q
2
𝑧 =
1
𝑅𝐶𝐶𝐶
Introduces zero that cancels out the pole generated by load
Best for power efficiency
Cc required can be large
Load conditions are not always controllable
Error in cancellation introduces pole/zero doublet which can lead to settling delays
RIN CIN
37
REQ CEQ
gmi
gmo
V
IN
VOUT
RLD CLD
RC
C
C

## Slide 37: Miller Effect
𝐶1 = 𝐶𝐹 1 + 𝐴
Identified in 1920 [2]
Negative feedback with a capacitor as the feedback element
Impedance seen at input is multiplied by gain
  Gain is also function of frequency
  A capacitor is effectively a short at high frequencies  phase is inverted (negative to positive)
C
C
F
-AV
i
v
-Av
V
-AV
C1
C2
𝐶2 = 𝐶𝐹
1+ 𝐴
𝐴
𝑑𝑉
𝑖 = 𝐶 𝑑𝑡
𝑖 = 𝐶 𝑑[𝑣− (−𝐴𝑉𝑣)] = 𝐶 𝑑𝑣[1 + 𝐴𝑉] = 𝐶
𝑑𝑡 𝑑𝑡 𝑀 𝑑𝑡
𝑑𝑣

## Slide 38: Miller Capacitor
CLD
|Zin|
RLD
RIN’~ CLD/(Cm*Gm)
Cpar  Cm
Cm
ML _ Gain ~ Gm  Rld 
Gm Cm
ML_ BW 

2 (Cld  Cm) Cpar  Cm
|ML|
RLD
CLD
Cpar
-Gm
Cpar
CLD
C
m
VOUT
VIN
ZIN
RLD
Cpar

## Slide 39: Two stage amplifier: Miller compensation
Uncompensated
Miller compensated CM=6pF
M=45°
M=0°
Very effective. Most commonly used compensation technique.
VIN-
VOUT
CEQ
VIN+
CLD RLD
gmi
gmo
CC

## Slide 40: Two stage amplifier: Miller compensation
Miller compensated
𝑝1 = 𝑔𝑚𝑜𝑅𝐸Q𝑅𝐿𝐷𝐶𝐶
1
𝑝
2
= 𝑔𝑚𝑜
𝐶𝐿𝐷
𝑧
1
𝐶𝐶
But introduced right half plane zero that increases magnitude and reduces
phase: = 𝑔𝑚𝑜
𝐶
Unity gain bandwidth: 𝜔
= 𝑔𝑚𝑖
𝐶𝐶
Dominant pole:
Output pole:
Poles moved apart due to Miller Compensation
p1
Uncompensated
p2

## Slide 41: Methods to eliminate the RHP zero
1
𝑧 =
1
𝐶
𝑔𝑚𝑜
𝑧
𝐶 ( 1 − 𝑅 )
There are two parallel paths two output  RHP zero in frequency response. RHPZ provides gain but phase loss  strong degradation of stability
  Can use a buffer to eliminate feed-forward action. Output impedance of buffer is not negligible.
  Can add a resistor to cancel out the zero. Typically select Rz to be equal to output transistor transconductance.
CC
CC RZ
time
voltage
42

## Slide 42: Two Stage Amplifier: Compensation Comparison
VIN-
VOUT
CEQ
VIN+
CLD RLD
gmi
gmo
CC
Uncompensated CLD=0
Uncompensated CLD=50pF
Shunt Compensated (5nF)
Miller Compensated (5pF)

## Slide 43: Outline
Introduction and background
Refresher on feedback theory, bode plots
Types of frequency compensation
A practical design example of a two stage amplifier
Alternative (advanced) compensation schemes
Practical tips and suggestions
Nested Miller Multipath nested Miller Advanced Miller topics Useful combinations

## Slide 44: Two Stage Amplifier Miller Comp (revisited)
Single dominant pole response set by CM as long as Miller loopgain (ML) is above 1
Second pole, at output node: ω2~G2/(CLD(1+Cpar/CM))
Load capacitance and parasitics impact ML bandwidth! Make CM>Cpar to maximize.
Feedforward causes RHP zero at ωz=G2/CM
Load resistance lowers Miller-loop gain!
Keep MLGain above 1
𝑀𝐿
𝐵𝑎𝑛𝑑𝑤𝑖𝑑𝑡ℎ
~
⋅
𝐺2 𝐶𝑀
2𝜋(𝐶𝐿𝐷 + 𝐶𝑀) 𝐶𝑝𝑎𝑟 + 𝐶𝑀
𝑀𝐿
𝐺𝑎𝑖𝑛
𝐿𝐷
~ 𝐺2 ⋅ 𝑅 ⋅
𝐶𝑀
𝐶𝑝𝑎𝑟 + 𝐶𝑀
G1
-G2
C
LD
C
par
CM
ML

## Slide 45: Cascoded Miller [8,9]
𝑀𝐿
𝐵𝑎𝑛𝑑𝑤𝑖𝑑𝑡ℎ
~
⋅
𝐺2 𝐶𝑀
2𝜋(𝐶𝐿𝐷 + 𝐶𝑀) 𝐶𝑝𝑎𝑟 +X𝐶𝑀
Adds gain to Miller Loop  much improved load capacitance drive
Blocks the RHP zero
Cascode gm (MP) must be higher than G1 to be effective
Adds LHP zero (improves phase margin)
Can have stability issues when CLD=CM (poor damping in Miller-loop)
Watch for stability during slew (avoid operating MP w/o current)
𝜔𝑧 = 2𝜋⋅ 𝐶
𝑔𝑚𝑀𝑃
𝑀
G1
-G2
CLD
Cpar
CM
ML
MP

## Slide 46: Split Cascoded Miller
Improved stability at Cld=CM
CM=CMa+CMb
CMa/CMb typically around 1 to 6
CMb reduces cap load drive but improves Miller loop damping at small CLD
Feedback around cascode (to increase gm) can eliminate need for CMb, but requires extremely high BW loop and stability during slewing not addressed
G1
-G2
CLD
Cpar
CMa
MP
CMb

## Slide 47: “Hybrid” Cascoded Miller
Increased (2x) effective Gm
Cascode Gm > input Gm
CM2x > CM1x for improved Cld drive
Avoid LHP zero by CM2a=CM2b and GmMNC=GmMPC
Pole/zero doublets can exist if not met
Must be evaluated for different load capacitances and load currents!
VIN-
V
OUT
VIN+
CM2b
C
M2a
CM1b CM1a
MPC
MNC

## Slide 48: Pole-Zero Doublets
time
voltage

## Slide 49: Cascoded Miller: Reduce Gain [10]
Reduce 1st stage gain by RS
Cascoded Miller reduces cap loading on first stage and increases Miller loop gain
Cld sets dominant pole at high CLD and BW is reduced
Can have issue to drive resistive loads (not enough gain)
Watch for stability issues at CLD=CM!
Many examples in literature to control impedance over frequency of internal high impedance node [10,12,13,14 ..]
G1
-G2
CLD
Cpar
CM
ML
MP
RS

## Slide 50: Cascoded Miller Comparison Simulations
Miller – no Cload Miller -- 500pF Cload Cascode – no Cload
Cascode -- 500pF Cload
Miller – no Cload Miller -- 500pF Cload
Cascode – 500pF Cload
Hybrid Cascode 0.5:0.5 -- 500pF Cload Hybrid Cascode 0.9:0.1 -- 500pF Cload
time
Vout

## Slide 51
Need more gain ….

## Slide 52: Additional gain stages
3 stages provide more gain, lower offset, wider input / output ranges, more current drive capability and lower distortion
They also lead to 3 high frequency poles that need to be compensated
For power efficiency always explore adding gain to existing stages (i.e. gain boost) before adding additional stages
More difficult to achieve in bipolar amplifier especially if need rail-to-rail operation (R)
Log Freq.
|A|
G
1
G
3
C
M1
CM2
G2
V
IN
CLD
R0 C0 R0 C0 R0

## Slide 53: Nested Miller Compensation
|A|
Log Freq.
3 stages  3 high frequency poles  “Nested Miller compensation”
  Set inner loop (G2-CM2-G3) ~2x amplifier bandwidth to assure CM1 ML gain.
  Output pole (G3/CLD) should be yet ~2x higher than that
Concept extends to 4 or more stages, with BW of the inner loops ~doubling with the addition of each gain stage
Each stage reduces bandwidth 2-3x
CM1
G1
G2
CLD
Cpar
-G3
Cpar
CM2
Assure Miller always across negative FB

## Slide 54: Reverse Nested Miller Compensation
Good for power efficiency
Strong CLD dependency due to limited gain in G3
Loading effects can be mitigated by isolation resistors
Non-inverting output stage!
55
G1
-G2
CLD
Cpar
G3
Cpar
CM1 CM2

## Slide 55: Feed-forward Compensation
Viola Schaffer
56
Cff bypasses G2 at high frequencies
Impedance looking into second stage is negative!
Look for distortion effects
G1
G2
CLD
Cpar
-G3
Cpar
CM1
Cff

## Slide 56: Feed-forward around a gain stage
LHP zero G2/Cff
|Vout/Vin|
Rs=R’!
CLD
Cff/(Cff+CLD)
57
Also known as a negative impedance converter
R’= -(Cff+CLD)/(Cff*G2)
Source impedance must be larger than |R’|
Cld
|Zin|
R’
+G2
Cpar
CLD
Cff
VOUT
VIN
ZIN

## Slide 57: Multipath NM (Feedforward) Compensation [3,4]
CM1
G1
G2
CLD
Cpar
-G3
Cpar
CM2
Gff
Combines the dynamic response and speed-to-power ratio advantage of a two-stage structure with the additional gain and better distortion of a three-stage amplifier
High frequency response dominated by feed-forward stage; offset and offset drift by the high gain path
Can be extended to multiple stages
Watch for large signal stability issues!
Low frequency behavior determined by high gain path
High frequency behavior is dominated by feedforward path. Introduces LHP zero into frequency response.
Each stage introduces a pole

## Slide 58: Multipath Nested Miller Compensation
Great for power efficiency
Introduces pole-zero doublet that can lead to settling issues. To exactly cancel pole-zero doublet:
Keep stich frequency close to bandwidth to mitigate effects of imperfect matching
Output impedance is complex! Can have issues with large load caps and driving ADCs.
G C
G1
ff M2
 CM1
|A|
[Hz]
100
80
60
40
20
0
100 102 104 106
108 Log Frequency
[dB]
[deg]
A 0
-90
-180
-270

## Slide 59: Multipath Nested Miller Compensation
Compare 3 stage amplifiers
  Uncompensated
  Nested Miller compensated
  Multipath Nested Miller compensated
In example (50pF CLD)
  3x better bandwidth
  40 degrees more phase margin

## Slide 60: External Techniques to Improve CL Drive
CL
RL
CF
RF
R
IN
RX
In-loop Snubber
VIN ZOUT
V
OUT
CL
RISO
V
Isolation
IN
Vout Rl
Z
OUT
C R
L L
VIN
VOUT
RS CS
CC
CIN
R
F
Input Cap loading
RIN
VIN
VOUT

## Slide 61: Output Impedance Frequency Response [16]
|ZO|
Capacitive
Inductive
Resistive
Log Freq.
Rail-to-rail output stages and multipath structures introduce complex output impedance
Region LO appears inductive and can interact with capacitive loading
ZLD
ZO
ZI
AVI

## Slide 62: Outline
Introduction and background
Refresher on feedback theory, bode plots
Types of frequency compensation
A practical design example of a two stage amplifier
Alternative (advanced) compensation schemes
Practical tips and suggestions

## Slide 63: Amplifiers have multiple feedback loops
[*] M. Degranuwe, J.Rijmenants, E.A.Vittoz, and D.Man,“Adaptive biasing CMOS amplifiers, ”IEEE JSSC,vol.SC-17,pp522–528, Jun 1982
[*] LM741 datasheet

## Slide 64: Tips to design for stability
Limit the number of gain stages
  Each gain stage decreases achievable bandwidth
  Consider gain (impedance) boost
  Consider nested gain structure
Three or more stages can lead to conditional stability
  Use clamps
  Control gain
Assure stability of each FB loop for overall system stability
  Keep local loops single stage if possible
Use compensation capacitors sparingly
Consider gain reduction
Watch for transient states (i.e. start-up; saturation in bipolar; current limit etc.)

## Slide 65: Gain (impedance boost)
a.
b.
c.
d.
GAIN
a.
b.
c.
d.
CL
VIN
V
OUT
VIN
VIN
VIN
V
OUT
V
OUT
V
OUT
CL
CL
VB
CL VB

## Slide 66: Building blocks for fast local loops[5,6]
Useful blocks to implement local control loops such as current limit
Don’t neglect common gate and current mode amplifiers

## Slide 67: Decreasing gain
A way to reduce impact of secondary poles
  Decrease gain by resistor
  Add capacitance / impedance to stabilize
I0
I0
RC
RC
CC
RL
RL
RL
I0=VGS/RC
Vi
Vi
Vi

## Slide 68: Nested gain structure
Parallel low gain path for speed and stability and high gain path for accuracy
MN
MP
Vout
Vin
[*] V.Schaffer, M.Snoeij, M.Ivanov, D.Trifonov, “A 36V Programmable Instrumentation Amplifier with Sub-20uV Offset and CMRR in Excess of 120dB at All Gain Settings” IEEE JSSC, vol.44, July 2009.

## Slide 69: Common conditions to watch for
Output stage operating conditions
  Voltage levels
  Sourcing or sinking current (change of transconductance)
  Close to triode
  CGS changes
  Class AB circuit can introduce delays and non-symmetricity
Start-up conditions
Loading effects (voltage and current dependency)
Parasitic capacitances (CGS CCB are voltage dependent)
Parasitic inductances (i.e. wirebonds)

## Slide 70: Pulsing nodes
Apply current pulse to high impedance nodes and observe settling behavior
Use ~10% bias current
Cadence – ‘Loop finder’ or ‘STB’ analysis
ITEST
time
Voltage, VX
VX

## Slide 71: Loading effects
Even simplest stage will introduce loading effects, parasitics and can transfer effects of subsequent stages
An ideal voltage controlled voltage source is very helpful for quick investigation (simulation only)
+G2
Cpar
CLD
Cff
VOUT
VIN
ZIN
CGS
CSB
RS
RL
CGD VOUT CGD
VIN

## Slide 72: Taming High Impedance Nodes
A practical method for taming high impedance nodes:
  Set Cc very large (1F) - BFC
  Choose largest Rc to get desired step response
  Decrease Cc until step response starts changing
[*] M.Ivanov, M.Ismail, V.Ivanov, “High Slew Rate Micro-Power CMOS OTA with Class AB Input Stage” IEEE Xplore
CC
RC

## Slide 73: Miller-Loop damping
Multiple gain stages in the Miller Loop require special attention
Many techniques exist to control impedance of high impedance nodes [10,12,13,14 ..]
Worst case may not be at max or min load current and capacitance!
Class AB biasing loop can degrade damping. This is load current dependent!
A suggested design approach:
  Find worse case Iload and Cload using parametric analysis and step responses
  Look for peaking in unity gain response
  Use STB analysis in Miller Loop (with all other outer loops opened) at worst case point. Keep phase margin>30 degrees (over corners).

## Slide 74: Large signal instability
Stable for small input signal / unstable for large step
Caused by linear range mismatch in 3- and more stage structures
Common cause of silicon revision
  To fix:
    Use passive or active clamps
    Transconductors with wide input stage
G1
G2
-G3
Gff

## Slide 75: Large signal stability
76
Stable AC
Unstable transient
frequency
|A| A
0dB
-180˚
time
Voltage

## Slide 76: Beware of Parasitic Effects
Bondwire inductance
Pad capacitance
CDG, CCB vs voltage
Bondwire
Bondpad
Drain-Source Voltage
Capacitance
CGD
CGS+CGD
FQP30N06L
CDS+CGD
CGS=0V

## Slide 77: Still Oscillates – where to start
Disconnect “unnecessary” loops if possible
Oscillation frequency
  Close to unity gain bandwidth
    Parasitics
    Feedforward RHP zero
    Loss of Miller loop gain
  Lower frequency
    Conditional stability
    Overdriven gain stage
    Saturated bipolar device
    Significant loss of Miller loop gain (i.e. cascode transistor)
  Higher frequency
    Parasitic inductances, negative impedance
    Unintended positive feedback
    Local feedback loops

## Slide 78: Papers to see at ISSCC 2021
31.4 ‘A Chopper-Stabilized Amplifier with -107dB IMD and 28dB Suppression of Chopper-Induced IMD’ T. Rooijers, S. Karmakar, Y. Kusuda, J.
H. Huijsing, K. A. A. Makinwa
5.6 ‘A 25A Hybrid Magnetic Current Sensor with 64mA Resolution,
1.8MHz Bandwidth, and a Gain Drift Compensation Scheme’ A. Jouyaeian, Q. Fan, M. Motz, U. Ausserlechner, K. A. A. Makinwa
5.5 ‘A 770 kS/s Duty-Cycled Integrated-Fluxgate Magnetometer for Contactless Current Sensing’ P. Garcha, V. Schaffer, B. Haroun, S. Ramaswamy, J. Wieser, J. Lang, A. Chandrakasan
5.8 ‘A 5V Dynamic Class-C Paralleled Single-Stage Amplifier with Near-Zero Dead-Zone Control and Current-Redistributive Rail-to-Rail Gm-Boosting Technique’ S-T. Koh, J-H. Lee, G-G. Kang, H. Han, H-S. Kim

## Slide 79: References
H. Nyquist, “Regeneration Theory,” Bell System Technical J., vol. 11, no.1, pp. 126-147, 1932.
John M. Miller, "Dependence of the input impedance of a three-electrode vacuum tube upon the load in the plate circuit," Scientific Papers of the Bureau of Standards, vol.15, no. 351, pages 367-385 (1920)
R.Eschauzier “Wide Bandwidth Low Power Operational Amplifiers”, Delft University Press, 1994.
R.Eschauzier, L.Kerklaan, J.H.Huising, “A 100-MHz 100dB Operational Amplifier with Multipath Nested Miller Compensation Structure”, IEEE JSSC, Dec. 1992, pp. 1709-1717.
V.Ivanov, I.Filanovsky , “Operational Amplifier Speed and Accuracy Improvement”, Kluwer, 2004.
V.Ivanov, “Analog Design Methodology – Practical Techniques for Frequency Compensation”, Mead 2020
N. Mehta, J.H.Huijsing, V. Stojanovic, “1-mW Class-AB Amplifier with -101 dB THD+N”, IEEE JSSC, Apr. 2019,
pp. 948-958.
J.Wieser, R. Reed, “Current Source Frequency Compensation for a CMOS Amplifier” US Patent 4,484,148.
B.K. Ahuja, “An Improved Frequency Compensation Technique for CMOS Operational Amplifiers”, IEEE JSSC, Dec. 1983, pp.629-633.
R.J. Reay, G.T. Kovacs, “An Unconditionally Stable Two-Stage CMOS Amplifier”, JSSC, May 1995, pp. 591.
G. Palumbo, S. Pennisi, “Design Methodology and Advances in Nested-Miller Compensation”, IEEE Transactions on Circuits and Systems, July 2002, pp. 893-903.
V. Dhanasekaran et al., “Design of Three-Stage Class-AB 16W Headphone Driver Capable of Handling Wide Range of Load Capacitance”, IEEE JSSC, June 2009.
A.K. Leung et al., “Damping-Factor-Control Frequency Compensation Technique for Low-Voltage Low-Power Large Capacitive Load Applications”, ISSCC 1999.

## Slide 80: References
X.Peng, W.Sansen, “AC Boosting Compensation Scheme for Low-Power Multistage Amplifiers”, IEEE JSSC, Nov. 2004.
D.M. Monticelli, “A quad CMOS single-supply op amp with rail-to-rail output swing”, IEEE JSSC, Dec. 1996.
C.Wells, M.Oljaca, “Modeling the output impedance of an op amp for stability analysis”, Analog Applications Journal
https://lpsa.swarthmore.edu/Nyquist/Nyquist.html
Dr Phil Allen – lecture notes
Art Key, Tim Green, “Analog Engineer’s Pocket Reference” www.ti.com/analogrefguide
B. Razavi, “Design of Analog CMOS Integrated Circuits”, McGraw-Hill, 2000, 2017.

## Slide 81: Examples of impedance control

## Slide 82: Examples to improve load capacitance drive

## Slide 83: 2-Stage Amplifier: Stable with any Cld
85