## Slide 1
Advance Analog and Mixed Signal Design
Lecture 01 /02 Introduction & Motivation
Dr. Neeraj Mishra
High Performance Electronics Lab
Electrical & Electronics Eng. Dept.
Birla Institute of Technology & Science Pilani, Pilani Campus

## Slide 2
Bio-Sketch
Name: Neeraj Mishra
Faculty Member: EEE Department BITs Pilani, Pilani Campus. (04 Dec 2024-)
Senior Researcher: Analog Mixed Signal IC Designer focus on high speed CMOS Design at ID Lab of imec & Ghent University Belgium (1 April 2023-20 Nov 2024)
Post-Doc: ADVISE Group, ESAT Department, KU Leuven ( Nov 2021-Nov 2022). (QS World = 76th Rank, QS Electrical & Electronics =39th Rank).
Research Topic: Radiation-hardened Time-to-Digital Conversion (RADTIME).
Advisor: Prof. dr. ir. Paul Leroux.
PhD : IIT Roorkee (Visvesvaraya PhD Scheme for Electronics & IT) (2015-2021). (QS World = 369th Rank, QS Electrical & Electronics = (150-200)th Rank)
Research Topic: High-Performance Ring Oscillator Using Separately Driven Inputs.
Advisor: Prof. Anand Bulusu.
M Tech : IIT Roorkee (2013-2015). (Gate Rank 346 in ECE)
Research Topic: Mechanical Stress aware design and layout of basic Analog building blocks.
Advisor: Prof. Anand Bulusu.
Job : (a) Engineer in Alcatel and Lucent Managed Solution Limited. (March 10 - May 13).
(b) Engineer in Railtel Corporation of India Limited (PSU Under Ministry of Railways). (June 08 - Feb 10).

## Slide 3
Motivation
Block diagram of a serial link with embedded clocking
Typical serial link architecture with embedded clocking used in data centre networks.
At the transmitter, a parallel data stream is serialized using a high-frequency clock.
A clock generator synthesizes this clock relying on an external crystal reference clock.
The receiver’s CDR retrieve the clock and data from the equalized signal.
Clock generation at TX and clock and data recovery (CDR) at RX require 35-50% of a link's power.
Block diagram of a typical wireless transceiver
The frequency synthesiser synthesizes the RF carrier and down-conversion signal at the receiver.
Synthesizers require 50% of transceiver power, and the rest is consumed by the CPU; mobile platforms include audio data converters and memory-required clocks.
Clock and frequency synthesisers play a key role and limiting their performance and power.
Wireline transceivers require many PLLs
LC-PLLs are used for low jitter BUT…
1) Susceptible to electromagnetic coupling
2) Narrow frequency range
3) `Mostly provide two phases

## Slide 4: Trend of Ever-Increasing Data Rate
PAM4 based transceivers drive the data rate beyond 100GBit/s
7nm CMOS technology enables power-efficiency <10pJ/conv.
Details of the wireline transceiver survey
28nm: NRZ
28nm: PAM4

## Slide 5: Introduction
ENIAC, U.S. Army, 1946
Size  Large hall (> 150m2) Power Consumption ≈ 150kW
Smart phone
Size  Your pocket Power consumption < 1W

## Slide 6: Electronics All Around Us

## Slide 7: Inside a I Phone

## Slide 8: What are Various Semiconductor Fab Types in Apple’s iPhone Supply Chain
Characteristics: EUV lithography High-performance, low-power logic Fabless model (Apple designs, TSMC manufactures) Examples in iPhone: Apple A-series SoC Custom Apple silicon blocks (CPU, GPU, NPU) 2. Memory Fabs a) DRAM Fabs Used for: LPDDR memory Companies: Samsung, SK hynix, Micron Fab type: Memory (DRAM) fabs Nodes: Specialized DRAM processes (not logic nodes) b) NAND Flash Fabs Used for: Storage Companies: Kioxia, Samsung, SK hynix, Micron, WD Fab type: 3D NAND memory fabs Characteristics: Vertical cell stacking (100+ layers) Highly capital-intensive, memory-only fabs 3. Image Sensor Fabs Used for: Camera sensors Companies: Sony (primary), Samsung (secondary) Fab type: CMOS Image Sensor (CIS) fabs Characteristics: Specialized pixel and photodiode processes Back-side illumination (BSI) Stacked sensor architectures 4. Display Fabs (Not traditional semiconductor fabs, but still “fab” environments) Companies: Samsung Display, LG Display, BOE Fab type: OLED / LTPO display fabs Characteristics: Large-area thin-film processing TFT backplane + OLED deposition Different from silicon wafer fabs Characteristics: Precision over scaling Long product lifecycles Examples in iPhone: Audio codecs & amps PMICs Motion & compass sensors 6. RF & Connectivity Fabs Used for: Cellular, Wi-Fi, Bluetooth Companies: Qualcomm (modems), Apple (Wi-Fi/BT), others Fab types: RF CMOS RF SOI Foundries: TSMC, Samsung, GlobalFoundries (varies) 7. Battery & Non-Semiconductor (Not Fabs) Battery cells (TDK, Sunwoda, Desay) → chemical manufacturing Cover glass (Corning) → materials & glass fabs Final assembly (Foxconn, Pegatron, Luxshare, Tata) → EMS factories
1. Advanced Logic (Foundry Fabs) Used for: Application processors (A-series chips) Company: TSMC Fab type: Advanced logic foundry Nodes: ~3nm / 2nm-class (A19 / A19 Pro timeframe)
2. Analog / Mixed-Signal Fabs
Used for: Audio, power management, haptics, sensors Companies: Cirrus Logic, Bosch, Asahi Kasei
Fab type: Analog / MEMS / mixed-signal fabs Nodes: Older, stable nodes (90nm–180nm+)

## Slide 9: And May Become Inside Us!

## Slide 10: Transistor Evolution
First transistor
Contacts separation ≈ 100µm Bell Labs, 1947
Trigate Transistor Fin width ≈ 8nm Intel, 2015

## Slide 11: Integrated Circuit Evolution
First IC
Only one transistor (+ R + C)! Texas Instruments (TI), 1958
Quad-core CPU
> 109 transistors!
Intel, 2017
≈ 11mm
≈ 13.5mm

## Slide 12: Moore’s Law
Moore’s law [1965]: Transistor count doubles every 1.5 years
Practically: It doubled every 2-3 years since the 4004 [1970s]
At the end of the day: It is exponential!
[Weste and Harris, 2010]

## Slide 13: Moore’s Law
Moore’s law [1965]: Transistor count doubles every year
Practically: It doubled every 2-3 years since the 4004 [1970s]
At the end of the day: It is exponential!

## Slide 14: Moore’s Law
Moore’s law [1965]: Transistor count doubles every year
Practically: It doubled every 2-3 years since the 4004 [1970s]
At the end of the day: It is exponential!

## Slide 15: The End of Moore’s Law?

## Slide 16: The Smartphone Plateau
[https://edition.cnn.com/interactive/2019/09/business/samsung-headquarters-south-korea/index.html]

## Slide 17: Growing Demand in New Applications

## Slide 18: IBM 2nm Technology
IBM announcement of 2nm technologies does not correspond to 2nm feature size!
  The individual nanosheets are 5nm in height, separated from each other by 5 nm.
[https://www.anandtech.com/show/16656/ibm-creates-first-2nm-chip]

## Slide 19: Analog vs Digital Signals
Analog: continuous in time and amplitude
Digital: discrete in time and amplitude
[Razavi, 2014]

## Slide 20: Why Digital?
Digital circuits are
  Less sensitive to noise (robust)
  Easier to store signals (digital memories)
  Easier to process signals (digital signal processing: DSP)
  Amenable to automated design
  Easier to port
  Amenable to automated testing
  Direct beneficiary of Moore’s law (down-scaling)

## Slide 21: Why Analog?
All the physical signals in the world around us are analog
  Voice, light, temperature, pressure, etc.
We (will) always need an “analog” interface circuit to connect between our physical world
and our digital electronics
Amplifier
A/D
Digital processing and storage
Transducer

## Slide 22: Why Analog?
Mechanical Transducers (Car/Airplane Sensors, MEMS, Nanopore)
[Y. Chiu, EECT 7327, UTD]
Digital Storage (DVD, Hard Disk, Flash)
Phone Lines, Cables (DSL, Cable Modem)
Audio
(MP3, Hearing Aid)
Video
(Dig. Camera, LCD TV, TFT Display)
E&M Waves (Cellphone, Radio, GPS)
Digital World (DT, DA)
Analog World (CT, CA)
Biochemical Sensors (Hazard detection, Drug Delivery, Lab-on-a-Chip)

## Slide 23: Sensors Proliferation

## Slide 24: Sensors Proliferation
Light sensor
Proximity
sensor
Touchscreen (capacitive sensor)
Accelerometer (capacitive sensor)
Gyroscope
(capacitive sensor)
Barometer (pressure sensor)
2 microphones (pressure sensor)
2 cameras
(image sensor)
Heartrate
sensor
Oxygen saturation
sensor (SpO2)
Temperature
sensor(s)
Compass
(magnetometer)
Fingerprint
sensor
Smart sensors market will grow from $46 billion in 2022 to $100 billion by 2027
[www.researchandmarkets.com, www.marketsandmarkets.com]

## Slide 25: Sensing Microsystems
01: Introduction
19
First accelerometer B&K, 1940s
Simple bulky transducer Acceleration  Voltage
4mm
3mm
ADXL350
Analog Devices, 2012 Complete system on a tiny chip
3-axis MEMS* accelerometer
Interface electronics
Analog-to-digital conversion
Memory
Control logic
Power management
Digital interface
*MEMS = Micro-Electro-Mechanical Systems

## Slide 26: Signal Processing Chain
Amp
A/D
Amp
D/A
Digital processing and storage
Power Management
Transducers
Physical world (sound, light, temperature, pressure, etc.)

## Slide 27: Electronic System Example: Wireless Transceiver
Amp
A/D
Amp
D/A
Digital processing and storage
Rx
Tx
EM Waves
Power Management

## Slide 28: Electronic System Example: Mixed-Signal Hearing Aid
0.5
0.1
0.01
Normalized frequency
0.001
0
-50
-100
-150
[dB]
ΣΔ
A/D
[Y. Chiu, EECT 7327, UTD]
DSP
AGC
Decimation Filter
ΣΔ
D/A
H-Bridge Driver

## Slide 29: Levels of Abstraction
[Razavi, 2017]

## Slide 30: IRDS Technology Node Definition
[IRDS ES, 2021]

## Slide 31: The End of Min Feature Size Scaling
[IRDS ES, 2020]

## Slide 32: But Still Too Many Steps! – IRDS 2020
[https://irds.ieee.org/images/files/pdf/2020/2020IRDS_BC.pdf]

## Slide 33: The different Ages of Scaling
[P. Gargini, IRDS, Intel]
1975 – 2000: Geometrical scaling
  Reduction of horizontal and vertical dimensions
  Improved performance of planar transistors
2000 – 2025: Equivalent scaling
  Reduction of only horizontal dimensions
  Introduction of new materials and new physical effects
  New vertical structures replace the planar transistor
2025 – 2040: 3D scaling
  Transition to complete vertical device structures
  Heterogenous integration
Our current bag of innovations can keep CMOS alive till 2040!

## Slide 34: Modern “Moore” Concepts
[Wolfgang Arden et. al., ITRS]

## Slide 35: Modern “Moore” Concepts: MtM
More than Moore (MtM): Diversification
  Adding functionalities not associated with transistor scaling to increase the value
    Sensors, MEMS, bio, passives, HV, RF, etc.
  3D integrated circuits
    Through silicon vias (TSVs) connect the dies together
[https://nhanced-semi.com/technology/about-3d-ics/]

## Slide 36: Why 3D ICs?
3D ICs enable heterogenous integration (logic + specialty)

## Slide 37: Why 3D ICs?
3D ICs enable heterogenous integration (logic + specialty)

## Slide 38: Chiplets
UCIe: Universal Chiplet Interconnect Express
https://www.uciexpress.org/
Higher yield + heterogenous integration

## Slide 39: Backside Power Delivery
https://www.youtube.com/watch?v=XnR9j7ljAx4&ab_channel=IntelTechnology

## Slide 40: Modern “Moore” Concepts
[Wolfgang Arden et. al., ITRS]

## Slide 41: Modern “Moore” Concepts: BM
Beyond Moore (BM): Beyond CMOS
  Find the next switch: many candidates exist
  Quantum computing
  Lots of funding by governments and industry
  But no commercial solution (reliable & cost-effective) available yet
[IRDS, BC, 2017]

## Slide 42: How Much it Costs?
TSMC planned 3nm fab is expected to cost $20 Billion.
The Moore’s law train will soon come to a stop.
  But not due to physical limits as many have expected!
No chance for Egypt in the semiconductor fabrication business (at least in the near future).
  What about other perspectives?
[Weste and Harris, 2010]

## Slide 43: Foundries with a Cutting-Edge Logic Fab
[https://en.wikichip.org/wiki/technology_node]
SilTerra X-FAB Dongbu HiTek ADI Atmel Rohm Sanyo Mitsubishi ON Hitachi Cypress Sony Infineon Sharp Freescale Renesas SMIC Toshiba Fujitsu TI Panasonic STM UMC IBM AMD Samsung TSMC Intel | ADI Atmel Rohm Sanyo Mitsubishi ON Hitachi Cypress Sony Infineon Sharp Freescale Renesas SMIC Toshiba Fujitsu TI Panasonic STM UMC IBM AMD Samsung TSMC Intel | Cypress Sony Infineon Sharp Freescale Renesas SMIC Toshiba Fujitsu TI Panasonic STM UMC IBM AMD Samsung TSMC Intel | Renesas SMIC Toshiba Fujitsu TI Panasonic STM UMC IBM GF Samsung TSMC Intel | Renesas SMIC Toshiba Fujitsu TI Panasonic STM UMC IBM GF Samsung TSMC Intel | Pan. STM UMC IBM GF Sam. TSMC Intel | IBM GF Sam. TSMC Intel | GF Sam. TSMC Intel | Sam. TSMC Intel | Sam. TSMC Intel | Sam. TSMC ? | ? ? ?
180 nm | 130 nm | 90 nm | 65 nm | 45/40 nm | 32/28 nm | 22/20 nm | 16/14 nm | 10 nm | 7 nm | 5 nm | 3 nm

## Slide 44: UAE Fab Cancelled

## Slide 45: GF Cancelled 7nm Plans

## Slide 47: Money is Not the Only Problem!

## Slide 48: India…

## Slide 49: The US…

## Slide 50: TSMC…

## Slide 51: Europe…

## Slide 52: Types of Companies in the VLSI Industry
IDM (integrated device manufacturer): Companies that design and manufacture integrated circuits (ICs)
  Ex: Intel, Samsung, Texas Instruments (TI), etc.
Fabless companies: Companies that focus on IC design only. They don’t have manufacturing capabilities.
  Ex: Qualcomm, Broadcom, Nvidia, etc.
  Product companies vs design services companies
Foundry companies (a.k.a. pure-play foundries or merchant foundries): Companies that focus on IC fabrication only, without having any in-house design capabilities.
  Ex: TSMC, Global Foundries, UMC, etc.
EDA companies: Companies that create the software tools used in IC design (EDA tools)
  Ex: Synopsys, Cadence, Mentor (now Siemens EDA), etc.

## Slide 53: Types of Companies in the VLSI Industry
[SIA Beyond Borders Report, 2016]

## Slide 54: The Semiconductor Ecosystem
[SIA Beyond Borders Report, 2016]

## Slide 55: The Evolution of the Semiconductor Ecosystem
[SIA Beyond Borders Report, 2016]

## Slide 56: Top Semiconductor Companies
[https://www.icinsights.com/news/bulletins/Intel-To-Keep-Its-Number-One-Semiconductor-Supplier-Ranking-In-2020/]

## Slide 57: More Companies Joining The Field!

## Slide 58: More Companies Joining The Field!

## Slide 59: Semiconductors Market
Semiconductor sales revenue worldwide (2019)
  ~ 484 billion USD
[https://www.statista.com/statistics/266973/global-semiconductor-sales-since-1988/]

## Slide 60: Electronics Market

## Slide 61: Electronics Market

## Slide 62: ICT Market
The 400+ billion semiconductor industry enables a 4,000+ billion information and communication technology (ICT) industry
Egypt’s total revenue (2019)
  ~ 57 billion USD
  ~ 31 billion (55%) goes for loans interests
  ~ 16 billion (28%) for loans repayment!
Only 10 billion USD remains
  We need 41 billion USD more in 2019 budget?!
[https://www.statista.com/statistics/268584/worldwide-ict-revenue-since-2005/]

## Slide 63: The Smartphone Plateau
[https://edition.cnn.com/interactive/2019/09/business/samsung-headquarters-south-korea/index.html]

## Slide 64: Lecture Plans

## Slide 67
The Wand L are the two important layout parameters that the designer can choose. In the on resistance equations, it seems that only W/L is important. The same W/L can be obtained in different ways. The transistor in the upper left and lower right corner have the same W/L, and thus the same on resistance. However, we will see later on that the lower right transistor has far more capacitance and thus will be a slower switch. Selection of W/L is crucial in analog IC design.